## Slide 1: Open-MCT Based iCub Telemetry Data Visualization Tool
Nuno Guedelha, Silvio Traversaro, Stefano Dafarra
AMI Research Increment 05-10-2021

## Slide 2: Motivation
Running an experiment…
  Hard time constraints
  Setup complexity
  Stress
Requires…
  Repeatability (automatized repetitive actions)
  Centralized control and visualization
  Flexibility (easy selection of telemetry data)
  Robustness (survive robot interface reboot)

## Slide 3: Motivation
Example walking demo
Battery status
External forces
Run individual plotters
cameras
RobotViz.
Reading YARP ports from terminal
Start YARP server
Run Yarpmanager
Load app config
Reading YARP ports from terminal
Running apps: yarpview, iCubGUI, WalkingModule
Monitoring
Control Inputs
Walking Coord.
Virtualizer
VR + gloves
Sensorised suit
Connecting ports
RPC client on terminal
Type RPC commands
Organize workspace
Overhead effort
Notes: Yarpmanager tool
The command-line utility "yarpmanager-console" and its graphical companions "yarpmanager" are tools for running and managing multiple programs on a set of machines.
Create apps from third-party apps, yarp modules and/or devices (yarpdev <device>)
Define app resources
Connect/disconnect ports

## Slide 4: Motivation
Issues
  Yarpmanager covers a lot
  Not handled yet:
    RPC commands
    YARP ports plotting
    YARP ports raw output
  Specific apps installed wherever you are visualizing the data!
    YARP
    Yarpview, iCubGUI, …
Which tool to solve these issues?
4
Run individual plotters
Reading YARP ports from terminal
Start YARP server
Run Yarpmanager
Load app config
Type RPC commands
Organize workspace
Overhead effort
CTRL Console
Visualizer
Robot

## Slide 5: Outline
why Open-MCT?
Open-MCT visualizer Overview: features and current limitations
Control Console Overview: a Remote RPC web interface
Architecture overview and protocols
  Connecting YARP data output ports to the visualizer web client
  Connecting the YARP RPC ports to the control console web client
Installation, parametrization and launching
Deployment and next steps

## Slide 6: why Open-MCT?
 | imgui | PlotJuggler | Foxglove | OpenMCT
Applications | 3D games / apps | Timeseries plots | Diag/viz robotics | Space missions
Features/Ergonomy | Smaller building blocks | Intuitive? Light interface | Robot 3D viz. visualization State transitions | Adv. Ploting, layout Plot <-> raw data State transitions
Integration / Portability | Any module integ. C++ libraries | Desktop app Websocket, CSV ROS | Desktop app ROS-Linux | Web app (websocket) Yarp.js
Modularity (UI, plugins) | Full freedom | Data source Plugins | ? | JS/JSON plugins Custom widgets num,image data
Base language / build tools | C++ | C++ | Node.js, Yarn, npm | JS, HML, Node.js, npm
Developper learning curve | Very slow | ? | ? | average
Notes: Positive
  Nice clear online plots, and easy to export to PNG, JPG formats.
  Easy to place component widgets on the main board.
  Easy switch between plots and table of function values.
  Easy full screen mode, native browser window zoom options.
Negative
  Exported plots are blurry.
  Local/UTC clock interface a bit confusing.
  in-window-zoom fixes timespan (there seems to be a static zoom only, freezing the data).
  No apparent axis options on the plots.
Javascript -> scripting language for web dev (JS in brwser)
Node.js -> open-source, JS runtime env (JS outside of browser)
Websocket API => multi-channel duplex over TCP connection
TCP -> layer 4
HTTP/Websocket -> layer 7
HTTP [half-duplex] / Websocket [full-duplex] -> facilitates real-time communication over TCP
ws|wss URI (Uniform Resource Identifier) -> ws://some-address.com:10000/a-channel
Supported by Google Chrome, Firefox, Microsoft Edge, Internet Explorer, Safari and Opera

## Slide 7: why Open-MCT?
 | imgui | PlotJuggler | Foxglove | OpenMCT
General Impression | Too complex | Many data source interfaces Only timeseries measurements | Promising ROS-Linux deps to tackle | Great portability Web based Evolving features
Notes: Positive
  Nice clear online plots, and easy to export to PNG, JPG formats.
  Easy to place component widgets on the main board.
  Easy switch between plots and table of function values.
  Easy full screen mode, native browser window zoom options.
Negative
  Exported plots are blurry.
  Local/UTC clock interface a bit confusing.
  in-window-zoom fixes timespan (there seems to be a static zoom only, freezing the data).
  No apparent axis options on the plots.
Javascript -> scripting language for web dev (JS in brwser)
Node.js -> open-source, JS runtime env (JS outside of browser)
Websocket API => multi-channel duplex over TCP connection
TCP -> layer 4
HTTP/Websocket -> layer 7
HTTP [half-duplex] / Websocket [full-duplex] -> facilitates real-time communication over TCP
ws|wss URI (Uniform Resource Identifier) -> ws://some-address.com:10000/a-channel
Supported by Google Chrome, Firefox, Microsoft Edge, Internet Explorer, Safari and Opera

## Slide 8: Open-MCT visualizer Overview
Adapted for planning and visualization
  streaming and historical telemetry data
  imagery
  timelines
Data plots in:
  fixed time span
  Sliding, fixed width time span
Data display can be toggled to table of values or plot.
5 component types free to create:
  Timeline of operations
  Folders
  Activity Modes (predefined variables updated at fixed intervals or scheduled timestamps).
  Clocks
  Custom grid stacked/Overlay plots
Notes: Open MCT can be adapted for planning and operations of any system that produces telemetry. Can display in one place:
streaming and historical data,
imagery,
timelines,
procedures,
other data visualizations.
NASA => use as:
Data visualization tool in support of multiple missions at the Jet Propulsion Laboratory.
Ames Research Center to support the development of lunar rover mission concepts
5 component types:
Timeline of operations: like a roadmap of tasks with a cursor indicating the present time.
Folders: can contain other components.
Activity Modes: Displays values of predefined variables updated at fixed intervals or scheduled timestamps (not sure).
Clocks: Displays UTC real time.
Stacked plots: 2-D plots arranged in a custom grid.

## Slide 9: Control Console Overview: a Remote RPC web interface
Feature Highlights
Same RPC interface as on terminal
Pre-filled defaults or placeholders
Reply text box for each interface
Re-used yarp.js-socket RPC API for Ping system command.
FT calibration interface
Walking Coordinator interface
Ping interface
VOCAB
Returned Data

## Slide 10: Combined Interfaces

## Slide 11: Architecture Overview and Protocols

## Slide 12: Installing, parametrizing and launching
🛠 Installing (README.md)
  NVM Node.js/npm version management
  Mamba dependencies (outside npm)
  robotology conda channel (YARP, Cmake, C++ compilers)
  https://github.com/dic-iit/yarp-openmct.git
  Npm
  Web browser
⚙️ Parametrizing ⏳
  Port configuration (Yarp & local names, type)
  Connection ON/OFF/Detect
  RPC commands
▶︎ Running
  Connect to robot network
  > npm start
  🌐 Open-MCT viz: <server-IP-address>:8080
  🌐 CTRL console: <server-IP-address>:3000

## Slide 13: Deployment and Next Steps
Tested on iCubGenova04
  Running modules and app from terminal
  Controle console
    RPC commands
    Network Ping
  Open-MCT based visualizer
    Individual iCub telemetry entry plots
    CTRL console
Issues analysis in progress…
Next steps
  Improve runtime stability
  Stacked & overlay plots
  Added 3D robot viz
  Imporve the control GUI

## Slide 14: Connecting YARP data output ports to the visualizer web client

## Slide 15: Connecting the YARP RPC ports to the control console web client